## Slide 1
Chapter 1 Introduction
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved

## Slide 2: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 2

## Slide 4: What’s the Internet?
mobile network
global ISP
regional ISP
home
network
institutional
network
Interconnected networks
Notes: 4

## Slide 5: Hardware view
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
Notes: 5

## Slide 6: More hardware: networked appliances
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use

## Slide 7
7.7 exabytes
daily
Data
view

## Slide 8
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, 802.11
Protocol view
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 9: What’s a protocol?
network protocols:
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 10
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force

## Slide 11: Service view
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 12: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 12

## Slide 13: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 14: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 15: Access net: digital subscriber line (DSL)
central office
ISP
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  < 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
  < 24 Mbps downstream transmission rate (typically < 10 Mbps)
DSL
modem
splitter
DSL access
multiplexer

## Slide 16
Access net: cable network
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing: different channels transmitted
in different frequency bands

## Slide 17
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
ISP
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office
Access net: cable network

## Slide 18
Access net: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet
wireless access point
wireless
devices
often combined
in single box

## Slide 19: Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  within building (100 ft – 200 ft)
  802.11b/g/n (WiFi): 11, 54, 450 Mbps transmission rate
to Internet

## Slide 20: Wireless access networks
wide-area wireless access
  provided by telco (cellular) operator, from10 miles to 1500 feet
  between 2Mbps and 1Gbps
  3G, 4G: LTE, 5G
to Internet

## Slide 21: Enterprise access networks (Ethernet)
typically used in companies, universities, etc
  10 Mbps, 100Mbps, 1Gbps, 10Gbps, 100Gbps transmission rates
  today, end systems typically connect into Ethernet switch
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 22: Physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gpbs Ethernet
  Category 6: 10Gbps

## Slide 23: Physical media: coax, fiber
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gpbs transmission rate)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 24: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  450Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 30 Mbps
satellite
  Kbps to Mbps channel (StarLink 100+Mbps download and 10+Mbps upload)
  270 to 20 msec end-end delay
  geosynchronous versus low altitude

## Slide 25: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 25

## Slide 26: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 27: circuit switching
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks

## Slide 28: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 29
A
B
.
.
.
packet switching

## Slide 30: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  ?
packet switching allows more users to use network!
N
users
1 Mbps link
…..
* Check out the online interactive exercises for more examples

## Slide 31: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 32: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 33
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion possible: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?
Packet switching versus circuit switching

## Slide 34: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
destination
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header
0111
0100

## Slide 35: Internet structure: network of networks
End systems connect to Internet via access networks
  Residential, company and university networks
Access networks in turn must be interconnected.
  So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 36: Internet structure: network of networks
Question: given a large numer of access networks, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 37: Internet structure: network of networks
Option: connect each access network to every other access network?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access network to each other directly doesn’t scale: O(N2) connections.

## Slide 38: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP

## Slide 39: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C

## Slide 40: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point

## Slide 41: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPs
ISP B
ISP A
ISP C
IXP
IXP
regional net

## Slide 42: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network

## Slide 43: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP

## Slide 44: Tier-1 ISP: e.g., Sprint
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence

## Slide 45: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 45

## Slide 46: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 47: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal
processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop

## Slide 48
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Four sources of packet delay
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
* Check out the Java applet for an interactive animation on trans vs. prop delay
Notes: 48

## Slide 49: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 50: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 51: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 52: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 53: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
Rs
Rs
Rs
Rc
Rc
Rc
R
. . .
. . .

## Slide 54: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 54

## Slide 55: Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  hardware, software
  protocols
Question:
is there any hope of organizing structure of network?

## Slide 56: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 57: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
message
M
Ht
M
Hn
frame

## Slide 58: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 58

## Slide 59: Network Security Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 62
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. Compromise hosts (botnet)
3. send packets to target from compromised hosts
Bad guys: attack server, network infrastructure

## Slide 63: Bad guys can sniff packets
packet “sniffing”:
  broadcast media (shared ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 64: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload
… lots more on security (throughout, Chapter 8)

## Slide 65: Chapter 1: roadmap
  1.1 what is the Internet?
  1.2 network edge
    end systems, access networks, links
  1.3 network core
    packet switching, circuit switching, network structure
  1.4 delay, loss, throughput in networks
  1.5 protocol layers, service models
  1.6 networks under attack: security
  1.7 history
Notes: 65

## Slide 66: Internet history
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet public demo
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 67
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
Internet history

## Slide 68
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Internet history

## Slide 69
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
Internet history

## Slide 70
2005-present
~750 million hosts
  Smartphones and tablets
Aggressive deployment of broadband access
Increasing ubiquity of high-speed wireless access
Emergence of online social networks:
  Facebook: soon one billion users
Service providers (Google, Microsoft) create their own networks
  Bypass Internet, providing “instantaneous” access to search, emai, etc.
E-commerce, universities, enterprises running their services in “cloud” (eg, Amazon EC2)
Internet history

## Slide 71: Introduction: summary
covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
you now have:
context, overview, “feel” of networking
more depth, detail to follow!